## Slide 1: Inner Tracking & Vertex Detectors
Frank Hartmann
Slides borrowed/stolen from many many people (including myself) 
Caveat: This is not a lecture about tracking; this is about how to design detectors to be good at the job!

## Slide 2: You will learn today
A reminder that a silicon sensor is simply an array of diodes - see detailed silicon sensor lecture yesterday
  Today with a bit different spin
Designing and operating a Tracker is a bit more complicated than placing sensors one after the other
Different Tracking Detectors as examples!
  Historic and future
    NA11, DELPHI, CDF, CMS; future CMS

## Slide 3: A simple array of diodes
A REPETITION WITH A SLIGHTLY DIFFERENT SPIN

## Slide 4: Historical aspects – Why use silicon?
Since 50ies large crystals for energy measurements
Need for fast and precise position measurements
  80ies charm quark tagging
  Late 80ies LEP experiments, vertex tracker
  90ies in hadron machines FERMILAB
  Today in all LHC experiments
Where are silicon sensors better suited than gas detectors?
Fast ~O(10ns); Precise O(5µm); very good energy resolution ~O(eV)
Silicon detectors gives momentum & vertexing,
which gives
b tagging
lifetimes
mixing background suppression
…… and a lot of great physics!
  Why wasn’t silicon used earlier?
    Needed micro-lithography technology  cost
    Small signal size (need low noise amplifiers)
    Needed read-out electronics miniaturization
      (transistors, ICs)
Take home

## Slide 5: Historical aspects II – Why use silicon?
In the post era of the Z and W discovery, after the observation of Jets at UA1 and UA2 at CERN, John Ellis visioned at a HEP conference at Lake Tahoe, California in 1983 “To proceed with high energy particle physics, one has to tag the flavour of the quarks!”
CDF; top quark discovery
LEP
Background reduction

## Slide 6: Evolution of Semiconductor detectors
50ties
Early strips
NA11
LEP & Tevatron
LHC
Beyond
scaling, scaling, scaling
HL-LHC
ATLAS/CMS
Tracker
HL-LHC CMS
Forward calorimeter???
FERMI
Notes: Scaling system up and Scaling electronics down was the main challenge in the past!
Miniaturization!

## Slide 7: The truth - Why Really Use Silicon
We benefit from the huge technological advances in the IT industry
  Pattern and structuring is industry standard
Even if the infrastructure is expensive, the basic ingredients are ridiculously cheap and exist in abundance
Air
Sand
The usefulness and success of silicon technology can be explained in a handful of keywords:
• existence in abundance
• energy band gap
• possibility to change gap properties by defined adding of certain impurity atoms
(dopants)
• the existence of a natural oxide

## Slide 8: Silicon properties – the numbers are simply right
And detector relevant:
Dense: the average energy loss and high ionized particle number with 390eV/μm ∼ 108 (electron–hole pairs)/μm is effectively high due to the high density of silicon.
  No charge amplification needed
very good intrinsic energy resolution: for every 3.6 eV released by a particle crossing the medium, one electron–hole pair is produced. (30 eV to ionize a gas molecule)
Very fast O(10ns)
Mechanical stability
  Self supporting

## Slide 9: How do Silicon sensors work? (Remember details last lecture)
Conductive, when electrons are missing here (holes)
Conductive, when electrons are here
New energy levels
Take home:  Dedicated material tuning possible!
Band gap
Dope
Reverse bias
Reverse bias diode = no free charge carriers
Electrical field helps to „drain/collect“ the created charges (e-h)

## Slide 10
BUT

## Slide 11: From Diode to Strip or Pixel Sensor
One diode
Produce more diodes!
Better: produce more diodes on a single substrate
  = Create a pattern on the substrate
  Reverse bias the pattern individually
strip
pixel/pad
Reminder:
Doping – Reverse Bias

## Slide 12: OK, let’s mount these arrays of diodes one after to other to get space points
How does it work in a FULL detector?

## Slide 13: What is the task of these detectors?
(2) Magnetic field bends the tracks
Momentum & energy
Measure track POINTs where charged particles traverses
Reconstruct tracks (interpolate points)
(3) With good 3D resolution and low occupancy
– isolate tracks in this mess
 Pattern recognition
(4) In conjunction with calorimeter identify particle (see first lecture)
(5) With even better resolution and lower occupancy (pixels)
- identify origin (vertex)

## Slide 14: Role and Challenges (I)
Measure the trajectory of the particle
  Several points (hits) along the track
  Fit a curve (helix or straight line)
    Determine momentum from the curvature in the magnetic field
    Track is mandatory for the particle flow algorithm and used for jet and MET reconstruction
      Remember an ECAL event without a track is a photon
Challenge at LHC
  High occupancy, radiation dose and data rates
  At LHC design luminosity (times 10 for HL-LHC)
    >20 interactions = 1000 tracks per pp crossing every 25 ns
Need large channel granularity to keep occupancy at acceptable level (percentage and below)
  Large numbers of electronic channels increase material and heat load
    Sensors, Power, cooling
  Minimize material to minimize multiple scattering of charged (and neutral) particle before the calorimeter and to avoid photon conversion

## Slide 15: Role of the Tracker (II) - Vertexing
Take home: This is the task of the pixel detector
Extrapolate track back to the point of origin
  Reconstruct
    Primary vertices (one among many)
      Distinguish primary vertices and identify the vertex associated with the interesting hard interaction
    Secondary vertices
      Identify tracks from tau-leptons, b- and c-quarks by lifetime tagging
        They decay inside the beam pipe
      Identify photon conversion and nuclear interactions
Just this one

## Slide 16
• Look for B vertex and measure decay length - distance between
primary and secondary vertices
• Most of decays of B mesons happen within 1-2 mm of interaction
point (cτ ~ 0.5 mm, stretched by relativistic time dilation)
• Need vertex detectors with excellent position resolution ~ 10 mm
D0
B
Primary Vertex
Secondary Vertex
K
π
µ
ν
Decay Length = lifetime
Example: Measurement of B Meson Lifetime

## Slide 17: Ok, how does it work?
What we get, when “simply correctly” interpolate and extrapolate the space points to tracks!
A bit computational brainpower later
Can you see the two B mesons?

## Slide 18
Identification of
b-quark event
~1 mm
=
~1ps
=
tb
Do we need such a high resolution?
Notes: Inside the beam pipe

## Slide 19: Increase in precision
0
1cm
x
=Beam crossing point

## Slide 20
Mean Lifetime of tau t=290 x 10-15 sec !! --> ct = 87 mm !?

## Slide 21
CMS double B jet CANDIDATE
Stating the obvious:
These second vertices are inside the beam pipe.
There are NO detector elements
Precision outside has to be good enough to extrapolate down here

## Slide 22: How to design to achieve the former? Impact Parameter Resolution
r1 small
r2 large
small sn = High intrinsic point resolution
Low mass
Tag b-quark - secondary vertex
Impact parameter d0
For two layers: Error propagated to interaction point
R1
R2
Take home

## Slide 23: There is no straight line!
Coulomb scattering on nuclei
  Charged particles only
Ergo, you want to have a massless tracker
Particles moving through the detector material suffer innumerable EM collisions which alter the trajectory in a random fashion (stochastic process)

## Slide 24
x
plane
Distribution of w is nearly
Gaussian (central 98%)
K. Nakamura et al. (PDG), J. Phys. G 37, 075021 (2010)
Multiple Scattering
w
d0=r tanw
Take home
MS
Higher momentum, p  less scattering
Best precision with
  small radius, r,
  and minimum thickness x
Particle incident on a thin layer, fraction x/X0 of a radiation length is bent by angle w
Notes: This is BAD
x – traversed thickness,
X0 – material radiation length

## Slide 25: Tracking has to take it into account!

## Slide 26: Leaving 90o incident angle Transverse Impact Parameter resolution all together Geometry and Material
sd0 depends
on geometry
on material,
decreases with pT
Tracks with θ ≠ 90 o
Sensor
This particle sees much more material
Take home:
track
track

## Slide 27
Measure sagitta s, from track arc  curvature, R
Measuring momentum
Circular motion transverse to uniform B field:
Relative momentum uncertainty is proportional to pT times
Sagitta uncertainty, ss. Also want strong B field and long path length, L
s
L/2
You want especially good point resolution s n
here
sS clearly defined by individual point resolutions and multiple scattering
Assume path length 1 m; B=2T
pT = 1GeV s = 7.4 cm R = 1.67m
pT = 10GeV s = 0.74 cm R = 16.7m
pT = 1TeV … ....
Take home:

## Slide 28
Momentum resolution (CMS)
Expected relative pT resolution
for muons vs |h| and pT.
b = material term
2008 JINST 3 S08004 CMS Experiment
(More material) 
Zoom – next slide
&
B-field wrong orientation
Notes: In truth the energy information for low/middle energetic electrons come from the tracker!!!

## Slide 29: Track Intrinsic Parameters - CMS
Hit (point) Resolution
Alignment
Multiple Scattering
  Mass is bad
Track parameter
resolutions
High momentum
Straight tracks
Point resolution!
Sagitta resolution
Low momentum:
Multiple scattering

## Slide 30
 Main features of silicon detectors:
• Fine granularity  very accurate position resolution
• Small amount of energy for signal quanta large signal
• Thin  close to interaction point
• Low mass  minimize multiple scattering
 True two dimensional detectors, like Silicon Pixel, are much robust in
high particle density environment
In most of the modern High Energy Physics experiment the
detector closest to the interaction point is based on silicon
pixel devices.
Again: Why Silicon Sensors for Trackers?
Small s
Small r1
Small

## Slide 31: A bit of history
Pre-LEP
  Tracking with Gas Detectors – no vertexing
LEP
  Gas Detectors = tracking
  Silicon Strips = vertexing + seeding
    Without vertexing = no decent b-lifetime
TEVATRON:
  Gas Detectors = tracking
  Silicon Strips = tracking (seeding) + vertexing
    Without vertexing = no top quark
LHC
  Silicon Strips = tracking
  Silicon Pixel= vertexing and tracking (seeding)
HL-LHC
  Silicon Strips = tracking
  Silicon Strixels = tracking + vertexing on ~mm precision
  Silicon Pixels = tracking + vertexing (seeding)
Pattern recognition better with finer granularity
Often – one has an inside-out + an outside-in tracking algo

## Slide 32: + Reality & Detector occupancy
Pixel detector occupancy is at least one order of magnitude smaller than strips. Occupancy depends on
  distance from collision point and
  channel size (pitch and length)
 Track seeding here
Example: pileup of 9 interactions.
- single pixel area = 100μm×150μm = 1.5×10-2mm2
- typical strip area = 10cm×100μm = 10mm2
Take home
This is DESIGN
~2%
~0,02%
Notes: Plots/maps from the Tracking paper

## Slide 33: Tracking is basically A ROAD SEARCH
Again: You want
No deviating tracks – no MS
  Algorithm compensates
Good granularity & low occupancy
  Only one track in the search window
  Low combinatorics
Track start at low radii
Large lever arm
Good point resolution
Any info/constraint helps:
  Vertex
  Info from other detectors
Kalman filters improves parameters with each hit
‘Borrowed’ from Francesco Ragusa
Often more than one possible road at the track points

## Slide 34: Tracking – https://cms.web.cern.ch/org/tracking-pog
Hits (clusters)
Seeds
Track building
Track fitting and selection
Unassigned hits
Strips
Pixel
Start
Serveral iterations
Slide from CMS Tracking Training Days
Combinatorics!?!?!
Granularity is key
Combinatorics!?!?!
Granularity is key
Notes: Not addressed explicitly the track fitting, the track selection and the track quality assignment (only high purity track hits are removed for the next iteration). It is a detail

## Slide 35: Iterative tracking features
Iterations beyond the
first one improve the
Acceptance either in
Pt or in displacement
And recover detector
Full hermeticity
Bla Bla computing power
Works with PU
PLOT
Situation gets more complicated with higher pile-up.
Lots of progress in software to counteract done and still necessary to be done!
displaced tracks
Only 2 pixel hits …
0: pixel triplets
1: low pt pixel triplets
2: pixel pairs. Recover gaps in pixel
3: displaced tracks with pixel triplets
4: mixed pixel/strip triplets
5: TIB/TEC
6: TOB/TEC
Slide from CMS Tracking Training Days
Notes: Plots from here: https://indico.cern.ch/event/316061/contribution/3/material/slides/3.pdf.
Name of iterations are defined in a backup slide
Violet area- tracks passing through cracks, therefore producing only 2 hits in pixels
Later iterations cover wider phase space
  Ideally profiting of the reduced hit multiplicity
  …but it is not so easy
   tighter requirements to build those tracks

## Slide 36: Or can we do tracking like this?
Look-up tables
  Associated Memories
  Number of patterns can easily ‘unmanageable’
Yes, we can
  This is what do in hardware for very fast response
    But it is a bit crude
    One needs to make a track-fit later
  Done at Level-2 trigger at CDF
  Will be done for ATLAS Track Trigger
  Is an option for the CMS Phase II trigger
    5ms / 12.8ms total trigger latency

## Slide 37: And the EVIL mass …
How to avoid Multiple Scattering – It’s not the Silicon

## Slide 38
Photon conversions
Conversions, g 
e+e , example from CMS
Two oppositely charged tracks
Consistent with coming from the same point
Consistent with fit to a common vertex, imposing zero mass
CMS-­PAS-­TRK-­10-­003
Slide from CMS Tracking Training Days
Have a guess!

## Slide 39
CMS conversions in pixel barrel
F distribution for conversions with |z|< 26cm, R< 19cm
 Compare pixel barrel structure in data and simulation
Spikes due to cooling pipes

## Slide 40: Tracker material (CMS TODAY)
Large material is considered the major drawback of the tracker. Nevertheless we should take into account that this large amount of material is instrumented.
Learn this lesson for the upgrade
Plot from JINST paper, actual numbers are even a bit higher

## Slide 41: Services: why they are heavy?
TIB/TID is challenging in terms of number of channels over volume density.
A very large number of service connections to be constrained in a very tight room:
- ordered layout difficult;
- tough handworked job.
Slide from CMS Tracking Training Days

## Slide 42: Last words on mass …
Earlier, I said: “It’s not the Silicon”
  This is true for a large detector as the LHC one.
  For an electron – positron detector even the mass of silicon is too much (services and mechanics are forbidden anyhow)
    Sensors should be thinned
    But not too thin to have enough signal (signal~thickness)
  Also remember the higher the momentum the less multiple scattering
    So what are you interested in??

## Slide 43: More things to think about
Alignment
Overlaps to allow alignment determination in the first place
Hermeticity

## Slide 44
Tracker Alignment
Consider a five-layer tracker
borrowed from F. Meier
To take home: CMS demonstrated, that initial perfect alignment is not crucial and can be determined later with tracks (but need collisions & cosmics)

## Slide 45
Tracker Alignment
A track goes through, leaving hits

## Slide 46
Tracker Alignment
All you really see are the hits, actually

## Slide 47
Tracker Alignment
How do you fix this?
Now, if your tracker is misaligned, the hits positions really look like this

## Slide 48
How do you fix this?
Tracker Alignment
If you assume the module positions are “ideal”, you see this

## Slide 49
How do you fix this?
Tracker Alignment
So your track really looks like this

## Slide 50
How do you fix this?
Tracker Alignment
To “align”, we keep track of the “residuals” between the hits and the
projected track positions (shown as ) for many tracks, then adjust
the positions of the actual detectors to minimize the residuals across the
whole tracker.

## Slide 51: Real Life implementations in the CMS Tracker
2D (3D) information
Hermeticity
Lorentz angle compensation
Data treatment

## Slide 52: Hermeticy
Tracker Inner Barrel
z
R
z=0
z
R
Tracker Endcap Disk
System is designed to be hermetic with respect to the interaction point
Being hermetic to other tracks would imply MORE material for tracks from the main interaction point
Slide from CMS Tracking Training Days

## Slide 53: Double Sided (DS) module - 2D
100 mrad
DS modules are two modules literally glued back-to-back!
DS modules eventually provide 2D hit information; in CMSSW tracking both the single 1D rechits are used (fitting) and the matched rechits (building, HLT) are used
Slide from CMS Tracking Training Days

## Slide 54: Overlap modules is necessary to guarantee hermeticity and to align the detector
Silicon detector
×
×
~5mm
overlap region
Here TIB Single Sided modules
Mechanical challenging

## Slide 55: Tracker Inner Barrel (TIB) - TODAY
~70cm
16 half cylinder shells, 135 to 216 modules. Front-back asymmetric, charge asymmetric since modules are tilted 9deg to compensate for Lorentz shift (different approach with respect to pixel detector)
ext
int
z=0
z
9deg
+
-
ext
int
x
y
Slide from CMS Tracking Training Days

## Slide 56: Pixel local reconstruction
Zero suppression performed on the readout chip discarding pixels below 3200e- equivalent signal. Pixel clusters are formed from adjacent pixels. (threshold will be 1600e- for pixel phase I)
Fast hit position reconstruction (track seeding and pattern recognition) consists in a slightly elaborated charge-based center-of-weight algorithm in both dimensions corrected for Lorentz shift.
More sophisticated template-based hit reconstruction is used for fitting. In the template-based reconstruction, the observed cluster charge distribution is compared to expected cluster charge shapes (templates) to estimate the hit position  Pixel simulation tool.
  Also helps a lot to accommodate all changes due to radiation effects
    Changes in electrical field; Lorentz angle
Too many channels:
Pixel sends only pulse height info and pixel address for pixels being hit

## Slide 57: Strip Local Reco
Front End Driver (FED):
subtraction of pedestal (level when no particle signal is present)
subtraction of common mode (event-by-event chip-wide collective fluctuation)
zero suppression: strip is retained if signal >5noise or if strip and one neighbours have a signal>2noise.
  Channels passing zero suppression are known as digis.
Later digis to cluster
  Position = center of charge
From APVs
  Signal on top of pedestal and noise
From FEDs
  Pedestal is subtracted and signal is kept if above the noise
From offline reconstruction
  Tighter cuts are applied on clusters on strips
  Signal amplitude is corrected for gain calibration
Notes: ATIQ UR RAMAN FROM NCP

## Slide 58: OFFLINE DPG – https://cms.web.cern.ch/org/tracker-dpg
DPG Task#1: Ultimate hit position correction
Alignment with Cosmics 2009 http://arxiv.org/abs/0910.2505
Tracker Performance 2010 http://arxiv.org/abs/1007.1988
Alignment with Tracks 2014 http://arxiv.org/abs/1403.2286
Lorentz Angle
Alignment
Hit resolution < pitch/√12
+

## Slide 59: Z – resolution pixels 100x150mm2 analog information – interpolation possible
Small angle:
Worst resolution
  single pixel
Best resolution
  ‘couple’ of pixels
Large angle
multiple scattering
Charge distributed on too many pixels some stay below hit threshold
Pixel has pre-simulated TEMPLATES knowing the most probable hit scheme
  Angle; Lorentz angle
Optimum –
‘couple’ of pixels hit
Single pixels
Hits smeared
Multiple scattering
Change barrel to forward config. Here

## Slide 60: Offline & Ops: Evolution of sensor parameters
Radiation changes:
  Electric field
  Defects
  Doping
To be compensated and corrected for (OFFLINE)
Lorentz Angle
Leakage currents
Depletion voltage
expectation
pixel

## Slide 61: The real World II The Problem Piles Up ..
The experimental reason for radiation …

## Slide 62
Challenge: overlapping events – pile-up
Multi Jet Event at 7 TeV
L=1029 yes …. But  L=1034

## Slide 63: And more pile-up
Not the end of the story; mind also the computing power you need to analyze this
Notes: Computing power

## Slide 64
2012
Even more PU
Precision allows
secondary vertex
identification

## Slide 65
Raw SET~2 TeV
14 jets with ET>40
Estimated PU~50
Even more PU

## Slide 66: The ultimate Pile-Up, so far
~10cm
78 reconstructed vertices in a special run in 2012
~10cm
ECAL hits HCAL hits
Charged tracks
78 reconstructed vertices in a special run in 2012

## Slide 67: Tracking and Vertexing – CMS Today
Very high efficiency
Superb vertex resolution
Tracker aligned to ∼5µm (pixel ~2µm)
Takes e.g. bow of sensors into account
The more tracks or better the more momentum parameters the better the vertex resolution

## Slide 68
And all combined
excellent resolution
Δp/p~2% @ 100GeV
Y resonances

## Slide 69: Examples
CMS
CDF
DELPHI
NA11
LEP
DELPHI
Hey, check it out - an early super detector
Oh, NA11

## Slide 70: Even a Bit Earlier

## Slide 71: First Strip Sensor
Today, I simply try to continue the good old tradition.
STRIPED SEMICONDUCTOR DETECTORS FOR DIGITAL POSITION ENCODING
E.L. HAASE, M.A. FAWZI*, D.P. SAYLOR and E. VELTEN
Institut für Experimentelle Kernphysik der Universität und des Kernforschungszentrums Karlsruhe, Germany
NUCLEAR INSTRUMENTS AND METHODS 97 (1971) 465-469;
The counters are large area ion-implanted detectors with a common aluminium contact and a front contact consisting of five or twelve gold strips separated by 0.2 mm.
Notes: When I was still in diapers
I could not resist to show this!

## Slide 72: First Silicon Strip Detector in HEP The NA11 silicon detector 1983
Experiments NA11/NA32 at CERN
Goal: Measure lifetime and mass of the charm mesons D0, D-, D+, D+s, D-s
Surface 24 cm2 (2” wafer)
1200 strip, 20 µm pitch
Ever 3rd/6th strip connected.
Precision 4,5 µm !
8 silicon detectors
(2 in front, 6 behind the
Target)
Ratio detector surface
to nearby electronics
surface 1:300 !
NIM205 (1983) 99

## Slide 73: First Silicon Strip Detector in HEP Event from NA11
Computer reconstruction of
a decay of D- K+π-π-
Flight path length (ctg)
used to deduce the lifetime
of the particle.
In later experiments these dislocated
vertices are used to identify - tag - heavy quarks.
Very Precise – Very Close

## Slide 74: DELPHI

## Slide 75: Si Detectors in Collider Experiments The DELPHI Vertex Detector
Sensor surface ~1,5 m2
888 Silicon sensors
Length ~1 m
Diameter ~ 20 cm
4 sensors daisy-chained

## Slide 76: DELPHI - Forward part
Great Fun!

## Slide 77: LEP: DELPHI
1997
3 double sided layers Rf, Rz
Extra forward strip sensors
Extra forward pixel
1994
1997
Even with the large size still clear bifurcation:
  Silicon gives Vertexing
  Gas gives Tracking
Notes: 10E0
Unique piece of Art and Beauty

## Slide 78: I believe the most complex boutique like detector – ever built
First time forward tracking established
Notes: I can never remember all the details – otherwise I would have studied biology

## Slide 79: Working with Neural networks at the end
A bb(bar) event:
Sophisticated reconstruction
algorithms necessary!
After reconstruction:

## Slide 80: CDF @ Tevatron
Silicon detector at a Hadron Collider – ARE YOU MAD?????

## Slide 81: From Nicola Bacchetta

## Slide 82: Collider Detector at Fermilab CDF
L00 – as close as possible to the beam
  ON the beam pipe
7 double sided sensor layers – 10m2
  Lowest mass possible
Tracking up to eta=2 with barrel configuration only
Tracking in Level-2 trigger

## Slide 83: The CDF Vertex Detector
One barrel (out of 3) of the CDF vertex detector SVX II
Notes: Every seen such a beauty?

## Slide 84: CDF – Intermediate Silicon Layers
Layer 6 & 7
Mind there is a gas drift chamber further out
I think one can say – first stand-alone tracking with silicon
Bifurcation
Silicon gives Vertexing & Tracking
Gas gives Tracking

## Slide 85: No top quark discovery without the vertex detector A “Golden” Top Event
tt(bar)  W+b, W-b(bar)
One W decays leptonically showing one lepton plus missing energy
Second W decays into qq(bar) producing two jets
Signature: one lepton, four jets of which two tagged b jets and missing energy
In 1994 the evidence of the top quark was published!
Phys. Rev. D50 (1994) 2966

## Slide 86: CMS
Most of the CMS strategies already discussed  Enjoy the photos

## Slide 87
  Sensor technology: n+ implant in n bulk
  100X150 mm2 pixel
  Operation: −10°C
40 MHz clock, Buffer data for 3.2μs for L1 accept
At r = 4.4cm
  60 MHz/cm2 at peak LHC luminosity (L=1x1034 cm)-2s-1
  Radiation tolerance: 3x1014 neq/cm2/yr
  Occupancy: 10-4
Tracking
3 space points to |η|=2.5
Seeds most tracking > 95% efficiency
Vertexing
18M forward and
48M barrel pixels
  Silicon PIXEL

## Slide 88: Half disc of Forward Pixels
Forward Pixel: 672 plaquettes installed

## Slide 89: Pixel Test Insertion into Tracker
70

## Slide 90: Pixel Barrel plus Endcaps
FPIX at CERN
Barrel Module

## Slide 91: And it is flexible – Long shutdown 1
Removed, repaired and re-inserted
  in 2009
Removed, repaired and re-inserted
  during 2013/2014

## Slide 92: BPIX insertion 12.2014

## Slide 93: FPIX Installation 12.2015

## Slide 94: Silicon Strip Tracker
Sensor Technology p-in-n
Design occupancy 1-2% - resolve & isolate tracks
  Outer cell size ~20cm x 100-200mm
  Inner cell side ~10cm x 80mm
  Pixel 100x150 mm2
  Operation -15C
  Signal / noise ~20 (above 10 after radiation)
  Radiation tolerance ~1.5x1014 neq/cm2
Best
resolution
Blue: double sided
Red: single sided
bent track
Changing from barrel to endcap because of material

## Slide 95
ROD INTEGRATION
Aachen
Karlsruhe
Strasbourg
Zurich
Wien
PETALS INTEGRATION
Aachen
Brussels
Karlsruhe
Louvain
Lyon
Strasbourg
Wien
Lyon
TEC assembly
TEC assembly
Pitch adapter:
Factories Brussels
TK ASSEMBLY
CERN TIF
Louvain
Strasbourg
Firenze
Wien
Bari
Perugia
Bari
Firenze
Torino
Pisa
Padova
TIB
-
TID INTEGRATION
FNAL
UCSB
TOB assembly
TIB/TID assembly
CERN
Pisa
Aachen
Lyon@CERN
Karlsruhe
FNAL
Sensor QAC
Module
assembly
Bonding
& testing
Sub-assemblies
UCSB
FNAL
Integration
into
mechanics
UCSB
Hamburg
Hybrids:
Factory-Strasbourg
Sensors:
Factories
Kapton:
FactoryAachen, Bari
Frames:
Brussels, Pisa,
Islamabad
Pisa
Perugia
FE-APV:
Factory  IC,RAL
Control ASICS:
Factory  Company (QA)
Brussels
HH
CERN
CF cutting
Factory
CF plates:
FactoryBrussels
CF cutting
Factory
Florence
Torino
Pisa
Move to Pit and Insert
Thank You Belgium
Thank You Belgium
Thank You Belgium

## Slide 96: Intermediate Structures: Petals
400 Different Pieces Makes one Petal, a Fairly Complicated Object:
We needed 288 in total!
Notes: ICB problem, thermal grease, back plane bonding, enforcement// ONE less mercedes per bin
31 LEP detectors had to be reworked 
DAQ petals due to missing thermal grease and backplane contact

## Slide 99
Some cables

## Slide 101: Optical Fibres Dressed onto the +End of the Tracker
90

## Slide 102: Multiservice Cables Dressed
90

## Slide 103: Tracker on the Way Down
6.5 tons
100 MCHF
2000 man years
100 m deep shaft below
Not insured ;-)
On one hook!
Several frightened physicists, including me!

## Slide 104: FLY IN

## Slide 105: Insertion of the CMS Tracker into the Heart of CMS

## Slide 106: DONE, TRACKER IS IN (Sunday 15.12.07 01.30)
95

## Slide 107: The CMS Upgrade
1 slide only
THE GREAT FUN for the next 10 years

## Slide 108: Requirements for the Tracker Upgrade
Radiation tolerance
  3000 fb-1 for Outer Tracker – Maintain possibility of replacing inner parts of the Pixel detector
Increased granularity
  Maintain occupancy ~1%, with 140 <PU>
Improved two-track separation
  Small pixels…
Reduced material in the tracking volume
  As good as we can
Robust pattern recognition
  Seeding capabilities in Outer Tracker
DAQ compatible with higher L1 rate and longer latency
  500 kHz ÷ 1 MHz, 12.5 μs
Contribution to Level-1 trigger
  pT modules in Outer Tracker
    Intelligent tracker
Extended tracking acceptance
  Up to about η=4 – concerns mostly the pixel detector
See earlier sections of this talk
See lecture Yesterday

## Slide 109
The CMS HL-LHC Tracker I lied – it’s two slides 
EE
Pixel detector - 4 layers at 3/7/11/16 cm with coverage up to η = 3.8 with 10 disks
4 m2 silicon sensors ≤ 150 µm physical thickness - 50x50 to 25x100 µm2 pixels optimization for performance
Outer Tracker - 6(5) layers(disks) - 2 sensor modules for trigger purpose
220 m2 silicon sensors ≃ 200 µm active or physical thickness - 15500 modules - 50M strips - 220M macro-pixels - 90/100 µm pitch - 2.5/5 cm strips - 1.5 mm macro-pixels in inner layers
Barrel  endcap
1.5 mm strips – pattern recognition
Tilted = no. of modules = mass
Double sensor modules to enable triggering
Low radius
Small pixel sizes
To reduce mass
DCDC powering
CO2
Occupancy:
Outer ~%
Inner 0.01%

## Slide 110: Summary, or how to have a perfect tracker
No mass – no power – no cooling
High channel granularity
Many, many layers
High redundancy
Ultra-high point precision
All 3D – pattern recognition
How to space layers
  Smallest inner radius; highest outer radius
  Highest resolution at low, middle and high radius
Obviously, all points are highly contradicting

## Slide 111: THE END Thanks a lot for the invitation It was a real pleasure!
And mind – AN ELECTRON
in the electromagnetic calorimeter without a track in the tracker
IS A PHOTON!

## Slide 112: Tracker Useful Bibliography
Technical Design Reports:
  Tracker TDR http://cds.cern.ch/record/368412/files/Tracker_TDR.pdf
  Addendum TDR http://cds.cern.ch/record/490194/files/cer-2244540.pdf
  TDR pixel phase I https://cdsweb.cern.ch/record/1481838/files/CMS-TDR-011.pdf
Papers
  SiStrip Tracker Commissioning and Tests at TIF http://arxiv.org/abs/0901.4316
  SiStrip Tracker Alignment at TIF http://arxiv.org/abs/0904.1220
  Track Reconstruction at TIF http://arxiv.org/abs/0902.1860
  Pixel Detector Commissioning with Cosmic Rays http://arxiv.org/abs/0911.5434
  SiStrip Detector Commissioning with Cosmic Rays http://arxiv.org/abs/0911.4996
  Alignment with Cosmics 2009 http://arxiv.org/abs/0910.2505
  Tracker Performance 2010 http://arxiv.org/abs/1007.1988
  Alignment with Tracks 2014 http://arxiv.org/abs/1403.2286
  Track Reconstruction 2014 http://arxiv.org/abs/1405.6569
Physics Analysis Summaries
  Momentum Scale http://cds.cern.ch/record/1279137/files/TRK-10-004-pas.pdf
  Material Budget Studies http://cds.cern.ch/record/1279138/files/TRK-10-003-pas.pdf
  Tracking Efficiency http://cds.cern.ch/record/1279139/files/TRK-10-002-pas.pdf
  Tracking and Vertexing http://cds.cern.ch/record/1258204/files/TRK-10-001-pas.pdf, https://cds.cern.ch/record/1279383/files/TRK-10-005-pas.pdf
CMS Notes
  SiStrip Tracker Commissioning CMS NOTE – 2009/021
CMS Detector at JINST
  http://iopscience.iop.org/1748-0221/3/08/S08004
Semiconductor Detectors - Basics
  G.Lutz, Semiconductor Radiation Detectors, Springer, Berlin (1999)
  H. Spieler, Semiconductor Detector Systems, 2005, ISBN-10: 0198527845 | ISBN-13: 978-0198527848
  F. Hartmann; Evolution of Silicon Sensor Technology in Particle Physics ; Springer Series: Springer Tracts in Modern Physics , Vol. 231
  Advances in Tracking Detectors; Annu. Rev. Nucl. Part. Sci. 2011. 61:197–221; 10.1146/annurev-nucl-102010-130052

## Slide 113: How to space layer?
Equal spacing
Local spacing
Good seeding 
  computing 
Linking problem 
MS very critical 
High combinatorics 
No linking problem
  good sagitta 
MS can be smoothed better 
This can be discussed for hours. Actually it is being discussed for years!
Extreme case:
  Very close spacing
    increases just point precision
    No real track anymore
Frankly:
  What looks, by eye, better to connect the dots?
What is better?

## Slide 114
The CMS HL-LHC Tracker I lied – it’s two slides 
EE
Pixel detector - 4 layers at 3/7/11/16 cm with coverage up to η = 3.8 with 10 disks
4 m2 silicon sensors ≤ 150 µm physical thickness - 50x50 to 25x100 µm2 pixels optimization for performance
Outer Tracker - 6(5) layers(disks) - 2 sensor modules for trigger purpose
220 m2 silicon sensors ≃ 200 µm active or physical thickness - 15500 modules - 50M strips - 220M macro-pixels - 90/100 µm pitch - 2.5/5 cm strips - 1.5 mm macro-pixels in inner layers

## Slide 115: Pitch/sqrt(12)

## Slide 116: Welcome to the real world (1)
A perfect cylindrical or disk-like sensitive layer (as often the tracker is described to simplify) would be marvellous; in the reality layers and disks are a complicated mosaic of rectangular or wedge shaped detectors.
Overlaps within the same layer/disk are needed to ensure hermetic measurement surfaces. Each layer and disk is designed to be hermetic with respect to straight tracks from the origin. To have overlaps modules has to be either tilted (pixel forward, tib barrel) or placed staggered in r, z, phi...
Consequences on the tracking software:
== some parts are strictly correlated to the geometry: in particular, where to look for next hit in propagation (navigation)? You cannot afford querying all modules. You need to navigate hierarchically modules according to criteria that are inevitably very dependent on the geometry.
== tough transition to new/different geometries, like the ones of the phase-II tracker (but we have time).

## Slide 117: Pixel local reconstruction
Zero suppression performed on the readout chip discarding pixels below 3200e- equivalent signal. Pixel clusters are formed from adjacent pixels, including both side-by-side and corner-by-corner combination. Each cluster must have a minimum charge of 4000 electrons equivalent.
Fast hit position reconstruction (track seeding and pattern recognition) consists in a slightly elaborated charge-based center-of-weight algorithm in both dimensions corrected for the expected Lorentz shift.
More sophisticated template-based hit reconstruction is used for fitting. In the template-based reconstruction, the observed cluster charge distribution is compared to expected cluster charge shapes (templates) to estimate the hit position. Templates are generated using a detailed pixel sensor simulation (Pixelav) to accurately take into account effects induced by the accumulated radiation that may result in biases up to 50microns. Templates depend on track parameters.

## Slide 118: Strip Local Reco
FED:
subtraction of pedestal (level when no particle signal is present)
subtraction of common mode (event-by-event chip-wide collective fluctuation)
zero suppression: strip is retained if signal >5noise or if strip and one neighbours have a signal>2noise. Channels passing zero suppression are known as digis.
Clusters are formed by digis.
Cluster seed: strip with signal>3noise; further strips are added if signal>2noise; cluster is kept if total charge (signal) is >5 times the cluster noise (the sum in quadrature of the noise of all strips in the cluster).
The cluster position is determined by charge-weighted average of strip positions corrected by Lorentz shift (10 to 20 microns in TIB and TOB respectively).

## Slide 119: Welcome to the real world (1)
A perfect cylindrical or disk-like sensitive layer (as often the tracker is described to simplify) would be marvellous; in the reality layers and disks are a complicated mosaic of rectangular or wedge shaped detectors.
Overlaps within the same layer/disk are needed to ensure hermetic measurement surfaces. Each layer and disk is designed to be hermetic with respect to straight tracks from the origin. To have overlaps modules has to be either tilted (pixel forward, tib barrel) or placed staggered in r, z, phi...
Consequences on the tracking software:
== some parts are strictly correlated to the geometry: in particular, where to look for next hit in propagation (navigation)? You cannot afford querying all modules. You need to navigate hierarchically modules according to criteria that are inevitably very dependent on the geometry.
== tough transition to new/different geometries, like the ones of the phase-II tracker (but we have time).

## Slide 120: Iterative tracking features
Iterations beyond the
first one improve the
Acceptance either in
Pt or in displacement
And recover detector
Full hermeticity
Bla Bla computing power
Works with PU
PLOT
Situation gets more complicated with higher pile-up.
Lots of progress in software to counteract done and still necessary to be done!
displaced tracks
Only 2 pixel hits …
0: pixel triplets
1: low pt pixel triplets
2: pixel pairs. Recover gaps in pixel
3: displaced tracks with pixel triplets
4: mixed pixel/strip triplets
5: TIB/TEC
6: TOB/TEC
Notes: Plots from here: https://indico.cern.ch/event/316061/contribution/3/material/slides/3.pdf.
Name of iterations are defined in a backup slide
Violet area- tracks passing through cracks, therefore producing only 2 hits in pixels
Later iterations cover wider phase space
  Ideally profiting of the reduced hit multiplicity
  …but it is not so easy
   tighter requirements to build those tracks

## Slide 121: Silicon Strips & Pixel
Principle similar to silicon strip sensors
Segmentation: Pixel(-diodes) instead of Strip(-diodes)
  Electronic on top of sensor to reach all pixels
Sensor
Ultrasonic wire
“bonding”
strips: just ONE coordinate,
Pixel: two coordinates 2D
“bump” bonding
channels: ~108 - 109
strips
pixel
Notes: CMS Streifen 206m² 10 Mio Kanäle / CMS Pixel 2m²: 44Mio Kanäle

## Slide 122: Modules
Amplifier
& shaper
Multiplexer
PLL – Sync
Ops Team:
Configure
every
module
Full analogue information
Strips
Pixels
Pixel – asynchronous – zero suppression
Strips - synchronous ergo full info
Notes: Full info – also zero

## Slide 123
Opto hybrid
FED in USC
Opto hybrids

## Slide 124: Many of These Structured Devices form a Tracking Detector
We measure
  Momentum (with magnetic field)
  Tracks
  Decay points
    Life time
    Flavour tagging
A cosmic
Resolution in the order of some µm
A collision